## Slide 1: A Reactive Online Optimization Based Whole Body Control for Quadruped Locomotion Over Challenging Terrain
Team 2
20185570 - Hong Seung woo
20183633 – Choe JongHun
[CE554] Mechanical Design of Civil Robot
October 5, 2018
Notes: 첫 페이지

## Slide 2: Table of Contents
Background Explanation
Research Topic
Research Plan
Future Work
Notes: 목차

## Slide 3: 1. Background Explanation
Applications of (Legged) Robot
- Personal service
- Disaster relief
- Extra..
Big themes of “Civil Robotics”
Notes: 다음과 같은 다족 로봇의 응용이 있다.

## Slide 4: 1. Background Explanation
Bipedal vs. Quadrupedal
- Stable
- Heavy payload
Recommendation: Quadrupedal
Notes: Stable: 다리가 4개이므로 기본적으로 bipedal보다 안정적, 통신이 끊기거나 갑작스러운 전원 차단에도 로봇의 com이 support polygon 바깥으로 나갈 확률이 적음.

## Slide 5: 1. Background Explanation
∴ Quadrupedal Robot Reliable Motion Control
Highly related with “Civil Robotics”
Notes: Stable: 다리가 4개이므로 기본적으로 bipedal보다 안정적, 통신이 끊기거나 갑작스러운 전원 차단에도 로봇의 com이 support polygon 바깥으로 나갈 확률이 적음.

## Slide 6: 1. Background Explanation
How Robot Works??
Notes: 로봇은 어떻게 움직이는가?

## Slide 7: 1. Background Explanation
Position based Robot
Torque based Robot

## Slide 8: 1. Background Explanation – Position based Robot
Control angle of each joint
Rigid and precise movement from high gain
Notes: Position based control robot에 대한 소개
IIT HyQ version 1.2(2011)
Joint의 각도를 주로 control함.

## Slide 9: 1. Background Explanation – Torque based Robot
Unitree Laikago
Control torque(current) of each joint
Notes: Torque based control robot에 대한 소개
Joint의 토크를 주로 control함.
여담: Torque based control robot과 Position based control robot의 차이 및 Torque based control robot의 필요조건.
과거에 Torque based control robot이 흔하지 않았던 이유.

## Slide 10: 1. Background Explanation – Torque based Robot
Obstacle
Compliance
M
Obstacle
M
Torque based controlled robot
Advantage of Torque control
저감속비, 고토크 모터 필요
모터 기술의 발달 등으로 최근에 들어와 활성화

## Slide 11: 1. Background Explanation
Plant
High-level controller
Low-level controller
Position control robot
Torque
control robot
control robot
General robot control framework
Notes: 전반적인(일반적인) 로봇 프레임워크 흐름에 대한 설명

## Slide 12: 1. Background Explanation – Simplified Robot Model
Full Body Model
Too complicate!
Take long computation time
Use simplified model

## Slide 13: 1. Background Explanation – Simplified Robot Model
Rigid Inverted Pendulum with Point Mass
Notes: HLC의 종류

## Slide 14: 1. Background Explanation – Simplified Robot Model
Full-Body Model
LIPM
SLPM
Centroidal Dynamics Model
Cart-Table Model
Notes: LIPM(Linear Inverted Pendulum Model)
SLPM(Spring Loaded Pendulum Model)
Centroidal Dynamics Model
Cart-Tabel Model
Full-Body Model

## Slide 15: 1. Background Explanation – High-Level Controller
HLC(High-Level Controller): Construct robot reference trajectory from sensor/feedback data
ZMP(Zero Moment Point) based HLC
CP(Capture Point) based HLC
Plant
High-level controller
Low-level controller
Position control robot
Torque
control robot
control robot
Notes: HLC의 종류

## Slide 16: 1. Background Explanation – High-Level Controller
What is support polygon
Smallest convex set including all contact points

## Slide 17: 1. Background Explanation – High-Level Controller
What is ZMP

## Slide 18: 1. Background Explanation – High-Level Controller
How ZMP based HLC works

## Slide 19: 1. Background Explanation – High-Level Controller
What is Capture Point
Station

## Slide 20: 1. Background Explanation – High-Level Controller
How CP based HLC works

## Slide 21: 1. Background Explanation – High-Level Controller
LLC(Low-Level Controller): Calculate joint angle or joint torque set from the CoM reference
IK(Inverse Kinematics)
ID(Inverse Dynamics)
Plant
High-level controller
Low-level controller
Position control robot
Torque
control robot
control robot
Notes: HLC의 종류

## Slide 22: 1. Background Explanation – High-Level Controller
IK(Inverse Kinematics)
ID(Inverse Dynamics)
Notes: HLC의 종류

## Slide 23: 1. Background Explanation – Inverse Kinematics
Notes: HLC의 종류

## Slide 24: 1. Background Explanation – High-Level Controller
Newton`s Law:
Newton`s Law: